## Slide 1: 1- Khaled Dia (20164726) 2- Majd Abu Nimeh (20166086) 3- Amin Abdullah Mahmoud Aqel (20166756) 4- Abdelrahman Mahmoud A.Mahmoud (20167318) 5-Ahmed Ali Abdelazim (20185942) 6-Asem Abdou (20193554) Instructor: Assist. Prof. Dr. Parvaneh Esmaili
Emergency Backup System For a critical load

## Slide 2: Project Outline
Introduction
The main Source and the ATS
Cooling System
Backup Generators
Load balancing and synchronization
Safety Circuits and system Connections
Remote Control and Control Panel
Refrences

## Slide 3: Introduction
When there is a sudden failure in the power supplied to any facility, we would find ourselves in a need of emergency backup system that is powered by diesel standby generators.
like in hospitals that need to be 24 hours supplying electricity as the oxygen needs to be flowing to the patients in every second.
In our project we developed a complete system to simulate the process of having backup generators working alongside with the main source
We used MATLAB, Simulink, MATLAB application designer, Other programming and markup languages like HTML, CSS, and JavaScript
Our system can be controlled using a control panel that was designed by the MATLAB application designer.
And can be controlled using a remote control via internet link from a web page.

## Slide 4: Introduction
Our system is supplied by three synchronous diesel-powered generators with 600 kW power generation as a backup system.
The critical load for the system requires 500 KW
In case the mains have failed, the generators shall supply, the power to the load and distribute the load among themselves.
In case one or more of the generators fails or become operational again, the working generators shall redo the load balancing.
When the grid network power becomes available, the generators shall stop.
All the generators should operate synchronously.
Every 8 hours, one of the generators should stop and cools the machine.

## Slide 5: Backup System Overview

## Slide 6: Next: We will start showing our system

## Slide 7: The main source and the ATS

## Slide 8: Main Source Block

## Slide 9: Main Source Parameters

## Slide 10: Automatic Transfer Switch

## Slide 11: ATS to Generators

## Slide 12: Grid is on

## Slide 13: Grid Switched off

## Slide 14: Generators Becomes Operational

## Slide 15: Cooling System

## Slide 16: Cooling Logic System

## Slide 17: Clock Waves

## Slide 18: Building Blocks
Repeating Sequence
If Condition
If Action Subsystem
Ideal Switch
Zero as Constant

## Slide 19: Results
Operational Events For Generators

## Slide 20: Backup Generators

## Slide 21: Generator Components

## Slide 22: Diesel Engine Governor

## Slide 23: Excitation Block

## Slide 24: Synchronous Machine

## Slide 25: Balancing and Synchronization
The Generators and load Balancing
Load Block and its values
The method used to Balance the generators and the load
Three Dark Lamps Method
The Waveform and Figure

## Slide 26: Load Balancing and Synchronization

## Slide 27: Load BLock

## Slide 28: Three Dark Lamps Method

## Slide 29: Balancing and Sycnhronization

## Slide 30: Safety Circuits and Power Connections
Transformer
Circuit Breaker
Bus Bars: to output the voltages and currents in per unit values or in volts and amperes
Measurements System

## Slide 31: Transformer

## Slide 32: Circuit Breaker

## Slide 33: Measurements

## Slide 34: Generator 1

## Slide 35: Generator 2

## Slide 36: Generators 3

## Slide 37: Remote Control and Control Panel

## Slide 38: Application Coding

## Slide 39: Coding

## Slide 40: Coding

## Slide 41: Remote control Via internet Link

## Slide 42: Remote control Via internet Link

## Slide 43: Any Questions?

## Slide 44: References
[1].”Three Dark Lamps Method” [online] Available: https://www.electronicshub.org/synchronization-of-generators / [Accessed: 5 jan 2020].
[2].”Synchronous Machine Implementation” [online] Available:https://ch.mathworks.com/help/physmod/sps/powersys/ref/synchronousmachine.html / [Accessed: 30 Dec 2020]
[3].”DEVELOPMENT of Diesel generators” [online] Available:https://www.sciencedirect.com/topics/engineering/diesel-generator / [Accessed: 6 Jun 2020].
[4].” Practical uses for generators” [online] Available:https://www.wpowerproducts.com/news/14-practical-uses-for-generators/[Accessed: 10 Jun 2020].

## Slide 45: The End
Thank you